## Slide 1: Anticoagulants
Cooper University Hospital
School of Perfusion
By:
Michael F. Hancock, CCP

## Slide 2: Anticoagulation for CPB
Since CPB circuit is a Thrombogenic surface that will cause platelet, complement, and coagulation activation, we must give drugs that reduce this activation
Heparin- primary anticoagulant for Cardiac Surgery
We must monitor the effect of our anticoagulant on a routine basis throughout the surgery to prevent clots from forming in our circuit

## Slide 3: Monitoring Anticoagulation
Activated Clotting Time (ACTs)- is a modified, accelerated Lee-White Whole Blood coagulation time
  An accelerator substance like Kaolin is added to the sample basically acts as the “Contact Activator”
  Maintaining ACTs >400 are recommended (480)
  ACTs should be taken 2-3 minutes after Heparin bolus
  Hypothermia increases ACTs
    Less Heparin clearance
  Rewarming lowers them
    More Heparin clearance

## Slide 4: Heparin
Heparin:
  A Polysaccharide extracted from mast cells of body tissue
  Acidic in nature, combined with Sodium in medicine
  Molecular Weight- 3,000 - 40,000 Daltons
    Mean Molecular Mass = ~15,000 Daltons

## Slide 5: Heparin
Site of Action-
  Binds to and potentiates AT-3 (Anti-Thrombin)
  AT-3 binds to thrombin and other factors to inhibit the clotting cascade
    AT-3 Inhibits activity of Factors IIa, VIIa, Xa, IXa, XIa
  If AT-3 deficient, must administer FFP to achieve an adequate ACT
Half-Life- 90 minutes
  Metabolized by the Kidneys

## Slide 6: Heparin
2 Types: Defined by extraction location
  Porcine intestinal mucosa (used at Cooper)
    Lower mean molecular weight
    More effectively inhibits Factor Xa
    Less binding to platelets due to lower molecular weight
    Linked with delayed bleeding post-op because Protamine doesn’t fully reverse the effect on Factor X
  Bovine lung
    Higher mean molecular weight
      More effectively inhibits Factor IIa (Thrombin)
      Great affinity for binding to platelets
      More effectively reversed by Protamine

## Slide 7: Heparin for CPB
Patient must be fully Heparinized for the surgeon to cannulate AND for us to go on CPB
  ACT greater than 480 seconds is required to go on CPB
    Causes 10-20% decrease in SVR when given
Units and Milligrams:
  Made up on varying molecular weights
  USP requires 120-140 units per mg
  Full Heparinization is considered to be 300-400 units per kg

## Slide 8: Reversal of Heparin
Protamine Sulfate
  Combines with acidic Heparin to form a salt complex, neutralizing the anticoagulant effect of both drugs
    Protamine alone has an anticoagulant effect
  Onset of Action- 5 minutes
  Half-life - 7 minutes
  Strong alkaline protein derived from Salmon Sperm

## Slide 9: Protamine
Protamine displays some transient Hypotension due to vascular dilation and negative cardiac inotropy
  Can be resolved with pressors and calcium
Other side effects are pulmonary vascular constriction, with loss of lung compliance and gas transfer and anaphylaxis
Side effects could be major in men that have had vasectomy due to endocrine hormone imbalances

## Slide 10: Protamine Reactions
Type I-
  Systemic Hypotension due to reduced SVR
Type II- Anaphylactic reaction
  Hypotension
  Pulmonary Vasospasm (high PA pressures)
  Edema
Type III- Catastrophic
  Pulmonary Vasoconstriction (very high PAs)
  Severe hypotension
  Dilated RV
  Death

## Slide 11: Heparin Rebound
Reappearance of heparin after complete neutralization of heparin with protamine
  Usually occurs in the first 4-6 hours after neutralization
  Due to:
    Large doses of heparin given, small dose of protamine
    Heparin bound to proteins released after surgery and back into circulation
    Faster clearance of protamine from body than heparin

## Slide 12: Heparin Alternatives
Used when patients have Heparin Induced Thrombocytopenia (HIT)
Argatroban- main alternative to heparin
  Direct Thrombin Inhibitor
  Rapid onset of action and half-life is 40-50 minutes
  Metabolized in the liver
  No antidote
  Measured by ACT and PTT
    1.5 – 3x baseline

## Slide 13: Heparin Alternatives
Bivalrudin (Angiomax)-
  Synthetic form of Hirudin
  Shorter half-life than Hirudin (safer)
    Half-life 25 mins
  Measured by PTT or ACT
    1.5 – 3 x baseline
  Excreted by kidneys
Recombinant Hirudin (Lepirudin)-
  Direct Thrombin Inhibitor
  Does not have an antidote to reverse
  Monitored by PTT
  Cleared by the kidneys

## Slide 14: Heparin Alternatives
Low Molecular Weight Heparin-
  4-8 hour half life
  Requires AT-3 as a cofactor
  Primarily inhibits Factor Xa
  Not reversed by Protamine
Danaparoid (Organan)-
  Mixture of heparin sulfate, dermatan, chrondroitin
  Catalyzes Antithrombin to inhibit Thrombin and Factor Xa
  Half-life is 4.3 hours

## Slide 15: Other Anticoagulants
Warfarin (Coumadin)-
  Competitively Inhibits Vitamin-K
    Inhibits the hepatic synthesis of Factors II, VII, IX,X
    Onset- 24-72 hours
    Full Therapeutic Effect- 5-7 days
    Half-life – 20-60 hours, variable
    Metabolized by Liver, excreted in urine
    Uses:
      Preventing Arterial Thromboembolism in Chronic AFib patients and Prosthetic Heart Valves patients
        Reduces risk by 2/3

## Slide 16: Coumadin
Surgery- must stop several days before surgery
  Give Heparin to bridge until surgery, LMWH usually
  Once Warfarin is stopped, it takes 2-3 days before INR is < 2.0, and 4-6 days for INR to normalize
    Once INR is < 1.5, surgery can be performed
  If surgery is Urgent, can give Vitamin K (Phytonadione)
    Drugs:
      Aquamephyton
      Mephyton

## Slide 17: Other Anticoagulants
Citrate Phosphate Dextrose (CPD)
  Indications- anticoagulate and preserve donor blood
  Mechanism-
    Citrate- binds Ca++
    Phosphate- helps maintain RBC 2,3-DPG
    Dextrose- provides RBC with energy
  Site of Action- Plasma and RBCs

## Slide 18: Anti-Platelet Therapy
Life span of a platelet is ~7 days
Platelets carry growth factors such as Platelet Growth Factor
  Idea behind PRP therapy
Two main groups of Platelet Inhibitors
  GlycoProtein IIb/IIIa blockers
  Adenosine Diphosphate (ADP) Receptors blockers

## Slide 19: GP IIb/IIIa Blockers
– IV Only
The GP IIb/IIIa receptor is one that allows cross-linking of platelets to form with fibrinogen to form the platelet plug
  Blocking this receptor prevents the thrombus formation
Has reduced the need of emergent CABG procedures in patients undergoing angioplasty or PCI

## Slide 20: GP IIb/IIIa Blockers
Drugs: IV Only
  Abciximab (ReoPro)- Half-life 30 mins
  Eptifibatide (Integrilin)- Half-life 2.5 hours
    Only IV
  Tirofiban (Aggrastat)- Half-life 2.2 hours
Patients requiring Cardiac Surgery:
  Stop GP IIb/IIIa Inhibitor
  Delay surgery, if possible, for up to 12 hours
  Maintain on Heparin therapy
  Ultrafiltrate on CPB if possible
  Transfuse platelets as needed

## Slide 21: ADP Receptor Blockers
    Block the ADP P2Y12 receptors necessary for activating the GP IIb/IIIa receptor
Drugs:
  Clopidogrel (Plavix)- Half-life 8 hours
  Prasugrel (Effient)- Half-life 4 hours
  Ticagrelor (Brilinta)- Half-life 12 hours
For patients requiring Cardiac Surgery:
  Stop ADP Blocker
  Delay surgery, if possible, for up to 5-7 days
  Maintain on Heparin therapy
  Ultrafiltrate on CPB if possible
  Transfuse platelets as needed

## Slide 22: Other Anti-Platelet Drugs
Aspirin (Acetylsalicylic acid)
  Mechanism of Action:
    Technically is an NSAID
    Cyclooxygenase Inhibitor
      Irreversibly inhibits COX
      COX converts Arachidonic Acid to Prostaglandins and Thromboxane A2
    Reduces the synthesis of Thromboxane A2
    Decreases platelet aggregation

## Slide 23: Aspirin
Dose Dependent- low dose gives anti-platelet effect without providing analgesia
Provides platelet inhibition within 60 minutes of administration
Half-life of ASA is only 20 minutes
  Effect of ASA on platelets is irreversible because platelets cannot regenerate new COX
  ASA effects last as long as the life of the platelet 7-10 days
  After a single dose of ASA, Platelet COX activity recovers ~10% per day

## Slide 24: Fibrinolytic System
Once the hemostatic clot has been formed, this mechanism is in place to break down the clot once the site of injury has begun to heal
Plasminogen- synthesized in the liver normally circulates in the plasma
  Conversion of Plasminogen to Plasmin activated by:
    Tissue Plasminogen Activator (tPA)
    Urokinase Plasminogen Activator (uPA)
Fibrin Split Products are formed when fibrinolysis occurs
  D-Dimer is a test that detects fibrin split products to diagnose hyperfibrinolysis

## Slide 25: Fibrinolytic Drugs
Streptokinase- infusion, antigenic, 20 min half life
Urokinase- infusion, not antigenic, 15 min half life
Alteplase (t-PA)- infusion, non antigenic, 5 min halflife
  Must be given within 3 hours of onset of stroke symptoms, 0.9 mg/kg will improve 30%
Reteplase- bolus, non antigenic, 15 min half life

## Slide 26: Anti-Fibrinolytic Therapy
Drugs can be given to block Fibrinolysis in the setting of bleeding
Used frequently in cardiac surgery to reduce blood loss
Can be an issue in patients with consumption coagulopathies that have excessive activation and of the coagulation and fibrinolytic systems
  Blocks fibrinolysis but increases chance of thrombosis

## Slide 27: Anti-Fibrinolytic Prophylaxis
Amicar (Epsilon-aminocaproic acid)- binds to plasminogen and plasmin and inhibits fibrinolysis
  Administered prior to CPB until 1-2 hours after CPB
  Continuously given
Tranexamic Acid- 10x more potent than Amicar
Aprotinin- inhibits proteolytic enzymes including plasmin, kalikrein and factor XIIa activation of complement
  No Longer Used- saw a lot of renal failure and neurological issues like stroke